Nearfield Loop Probes

---
Nearfield Loop Probe
- Variants available for both H- and E-fields
- Short range RF pickup
- Typically used for EMC testing
  - Precompliance
  - Tracking down source of a failure

---
Nearfield Loop Probe (Tekbox TBPS01)
20mm H-field
10mm H-field
5mm H-field
5mm E-field

---
Nearfield Loop Probe
- Coupling varies with distance from DUT
  - Not useful for quantitative intensity measurements
  - But allows precise physical location of emitter to be found
- Often used for ratiometric EMC measurements
  - Place probe a fixed distance from DUT
  - Compare field strength before / after some change
- Ratio doesn’t scale 1:1 with far field strength
  - But usually close enough if you add some safety margin

---
Nearfield Loop Probe
- Start with sensitive probe for long range scanning
- Move to smaller one to pin down exact source
- May need external LNA for weak signals

---
Nearfield Loop Probe: Strengths
- Very broadband (most go to several GHz)
- Only real option for benchtop EMC testing
  - Calibrated antenna in anechoic chamber is definitive
  - But they’re big and expensive!
- Allows spatial location of emitter to be found

---
Nearfield Loop Probe: Weaknesses
- Very sensitive to exact position
  - Not useful for quantitative measurements
- Ultra specialized
  - Not useful for much besides EMC testing

---
Nearfield Loop Probe: When to use
Identifying the source of an EMC problem